## Slide 1: Bending Moment and Shear Force Diagrams 28 March 2017 Atul JAIN

## Slide 2: Analysis of Beams
Beams are commonly used structural members
Characteristics of beams
- Long
- Straight
- Usually subject exclusively to normal loading
Typically made of Steel, Aluminum in modern applications, wood was the favored material historically

## Slide 3: Classification of beams
According to cross-sectional shape

## Slide 4: According to support
Three major types of statically determinate beams- to be considered today

## Slide 5: Shear Force and Bending Moment
Imagine a randomly loaded beam
Let us make a section a point C
Drawing FBD for both sides of the section
There is Shear force V and Bending moment M
The value of V and M would depend on where “C” was chosen
The plot of V and M as a function of x is shear force and bending moment diagram

## Slide 6: Sign Convention
The bending moment is positive (+) when the external forces acting on the beam tend to bend the beam at the point indicated in fig
The shear is positive (+) when external forces acting on the beam tend to shear off the beam at the point indicated in fig

## Slide 7: Why BM and SF are important?
We calculate Bending Moment M and Shear force F at every point.
It can be shown
Also, useful for quick design
Greater the bending moment, greater will be the area of reinforcement required and greater the depth of the member required in the plane of bending.

## Slide 8: How to draw BM and SF
Step 1: Calculate the reactions at A and B
Step 2: Draw a section at before every load discontinuity
Step 3: Going left to right draw the FBD of each section
Step 4: Calculate and plot V, M as a function of x for each section
Section AD:
V = ½ P
M= ½ Px
Section AE:
V = -½ P
M= ½ P(L-x)

## Slide 9
Section AD (D lies between A and C):
V = ½ P
M= ½ Px
Section AE (E lies between C and B):
V = -½ P
M= ½ P(L-x)
A
C
B

## Slide 10: Distributed force
Force is continuous, any one section is enough
For distributed load, replace distributed force by concentrated force as shown
V = -wx
M = -1/2wx2

## Slide 11
Load | 0 | Constant | Linear
Shear | Constant | Linear | Parabolic
Moment | Linear | Parabolic | Cubic
Common Relationships

## Slide 12
Load | 0 | 0 | Constant
Shear | Constant | Constant | Linear
Moment | Linear | Linear | Parabolic
Common Relationships
M

## Slide 13: Problem I
Step 1: Calculate the reactions at A and B
Step 2: Draw a section at before every load discontinuity
Step 3: Going left to right draw the FBD of each section
Step 4: Calculate and plot V, M as a function of x for each section

## Slide 14: Problem II
Step 1: Calculate the reactions at A and B
Step 2: Draw a section at before every load discontinuity
Step 3: Going left to right draw the FBD of each section
Step 4: Calculate and plot V, M as a function of x for each section

## Slide 15: Problem III

## Slide 16: Problem IV
Q: Assuming that the reaction of the ground is uniformly distributed, draw the shear and bending-moment diagrams for the beam AB and determine the maximum absolute value (a) of the shear, (b) of the bending moment.

## Slide 17: Problem V
Step 1: Calculate the reactions at A and B
Step 2: Draw a section at before every load discontinuity
Step 3: Going left to right draw the FBD of each section
Step 4: Calculate and plot V, M as a function of x for each section
W = 12kN

## Slide 18: Problem VII
Step 1: Calculate the reactions at A and B
Step 2: Draw a section at before every load discontinuity
Step 3: Going left to right draw the FBD of each section
Step 4: Calculate and plot V, M as a function of x for each section

## Slide 19: Problem VI
Step 1: Calculate the reactions at A and B
Step 2: Draw a section at before every load discontinuity
Step 3: Going left to right draw the FBD of each section
Step 4: Calculate and plot V, M as a function of x for each section
Q: Draw the shear and bending-moment diagrams for the beam and loading shown, and determine the maximum absolute value (a) of the shear, (b) of the bending moment.