## Slide 1: Shafts
Shafts: A rotating Member.
        Usually has circular cross-section (solid or hollow)
        Transmits power and rotational motion
        Houses other components
Components: Gears, Pulleys, Flywheels, Clutches – are mounted on
          shafts. Transmit power
Attachment: via Press-fit, Tapered fits, keys, pins, set-screws, splines –
          for attaching machine elements to shafts
Mounted on: Bearings (rolling contact, journal bearings)
Couplings: Transmit power from driver shaft (motor) to driven machine
        (gear box, wheel)

## Slide 2: Shaft Design For Stress
Look for critical stress locations – Compare stresses at various locations
Most of the times shafts are under combined loading – compute alternating and mid range components of von-Mises stress
If axial stress is significant use Equations (6.55) and (6.56) from book
For fatigue use modified Goodman criterion
Always check for static yielding

## Slide 3: Shaft Design For Stress
Stress Concentration – Shafts have steps, grooves, shoulder relief etc.,
              for mounting gears, bearings, …
Challenge – Shaft diameter is not known apriori
Way out:
(Can start with the worst case scenario)
Also for keyways: Table 7-1 for static stress concentration factors
            (select as starting values – 1st iteration)
Shaft Deflection: Table 7-2 for maximum permissible deflection and slope
Complete geometry of the shaft must be worked out for analysis
Also check for failure of keys, pins,
For key, pin sizes: Tables 7-5, 7-6, 7-7, 7-8

## Slide 4: Shaft Vibration – Critical Speed
When the shaft is of uniform diameter.
For stepped shaft (segments of uniform diameter).

## Slide 5: Influence Coefficient
Forces act due to mounting of machine elements (gears, pulleys, etc.)
For loads at multiple location – obtain influence coefficient matrix
 |  | Load location |  |  | 
 |  | 1 | 2 | 3 | ... j
Deflection location | 1 | d11 | d12 | d13 | d1j
 | 2 | d21 | d22 | d23 | d2j
 | 3 | d31 | d32 | d33 | d3j
 | i | di1 | di2 | di3 | dij
Also – From Reciprocity Theorem
dij = dji (symmetric)

## Slide 6: Influence Coefficient
Displacement at locations due to forces of magnitude Fj
This is an eigenvalue problem !!! The above has three eigenvalues
The CRITICAL SPEEDS

## Slide 7: Influence Coefficient
From the characteristic equation can show
To include shaft mass:

## Slide 8: Additional Topics
Miscellaneous shaft components: Section 7-7
Shaft limits, tolerances, and fits: Section 7-8