## Slide 1
Micro Car based on MEMS electrostatic Actuator
The Micro transportation system based on MEMS electrostatic actuator. The micro car has a dimension of 0.2 mm x 0.03 mm (W x T). The 'road' system consists of straight, turning and T-junction modules.
D. V. Dao, P. H. Pham and S. Sugiyama, “Multi-Module Micro Transportation System Based on Electrostatic Comb-Drive Actuator and Ratchet Mechanism”, IEEE/ASME J. Microelectromechanical Systems (JMEMS), Vol.20/1, 140-149, (2011)

## Slide 2
Resistive heating of NiTi Shape memory alloy wire

## Slide 3
In situ transmission electron microscope (TEM) video (accelerated 10 times) of nucleation and self-organization of a high-density carbon nanotube network from catalytic iron nanoparticles, forming a vertically aligned forest.

## Slide 4: Clarification of the terms
Processing:
Casting route, Powder metallurgy route, Sintering, Doping, Vapor deposition
Thermal & Thermo-mechanical treatment (Forming): Forging, Rolling, Extrusion, Joining
Structutre: Arrangement of material’s internal components
Subatomic:
Atomic/ crystal
Microscopic
Macroscopic

## Slide 5
10-15
10-9
10-3
103
Time (s)
Length (m)
10-10
10-8
10-6
10-4
Structure of matter
Structure & behavior of defects
Collective dynamics of defects
Microstructure
Continuum
Paradigms of multiscalings

## Slide 6: Properties
Magnitude and Type of materials’ response to the
environment and external forces.
Mechanical
Electrical
Magnetic
Thermal
Optical
Chemical

## Slide 7
Atomic Structure and Interatomic bonding

## Slide 8
Electron, Proton, Neutron – Masses and charges
Atomic mass/ weight (atomic mass unit)
Atomic number, Avogadro number, mole
Electrons in solids – Concepts of Classical mechanics vs. Quantum mechanics
Bohr atomic model -- Energy levels/ states
Wave mechanical model
Quantum numbers – Electron states (Values of energy that are permitted for electrons)
Pauli exclusion principle (The manner in which these states are filled with electrons) – Each electron state can hold no more than 2 electrons, which must have opposite spins
Electronic configuration
Ground state
Valence electrons (that occupy the outermost shell)
Recapitulate the following basic concepts yourself

## Slide 9
Recapitulate the electronic configurations of atoms from the book

## Slide 10
Valence electrons determine all of the following properties
    Chemical (stability/ chemical reaction/ atomic bonding)
    Electrical
    Thermal
    Optical

## Slide 11: Electronic Structure
Electrons have wavelike and particulate properties.
  This means that electrons are in orbitals defined by a probability.
  Each orbital at discrete energy level determined by quantum numbers. Quantum # Designation
  n = principal (energy level-shell) K, L, M, N, O (1, 2, 3, etc.)
  l = subsidiary (subshell) s, p, d, f (0, 1, 2, 3,…, n -1)
  ml = magnetic 1, 3, 5, 7 (-l to +l)
  ms = spin orientation ½, -½
Position of an electron
Shape of the subshell
# of energy states for each subshell
Related to
Spin moment of an electron

## Slide 12: Electron Energy States
1s
2s
2p
K-shell n = 1
L-shell n = 2
3s
3p
M-shell n = 3
3d
4s
4p
4d
Energy
N-shell n = 4
• have discrete energy states
• tend to occupy lowest available energy state.
Electrons...
Adapted from Fig. 2.4, Callister 7e.

## Slide 14
Recapitulate the Periodic Table from the book

## Slide 15
Recapitulate the Periodic Table from the book
Electro-negativity
Atoms are more likely to accept electrons if their outer shells are almost full, and if they are less “shielded” from (i.e., closer to) the nucleus

## Slide 16: Bonding Force and Energies
Bonding Energy: E0
E0, Shape of the curve =
f(material, type of atomic bonding)
Properties: L/S/G; Melting Point, Modulus of elasticity, Coeff. Of thermal expansion

## Slide 17: Properties From Bonding: Tm
• Bond length, r
• Bond energy, Eo
• Melting Temperature, Tm
Tm is larger if Eo is larger.
r
o
r
Energy
r
larger Tm
smaller Tm
Eo
=
“bond energy”
Energy
r
o
r
unstretched length

## Slide 18: Properties From Bonding : a
• Coefficient of thermal expansion, a
• a ~ symmetry at ro
a is larger if Eo is smaller.
=
a
(
T
2
-
T
1
)
D
L
L
o
coeff. thermal expansion
D
L
length,
L
o
unheated, T
1
heated, T
2
r
o
r
lower a
higher a
Energy
unstretched length
Eo
Eo

## Slide 19: Atomic Bonding
Covalent
  sharing electrons
  strong
  directional
Primary
Ionic
  trading of elecrons
  electrostatic attraction
  strong
  non-directional
Metallic
  metal ions in sea or electrons
  moderately strong
  non-directional
Nature of the bonds = f (Electron structure of constituent atoms)
Atoms want to assume stable electronic structure

## Slide 20: f09_02_pg27
IONIC BONDING
Ionic
  trading of electrons
  electrostatic Columbic attraction
  Strong: Large bonding energy: between 600 – 1500 kJ/mole
  non-directional
Hard, Brittle, Insulators
Notes: f09_02_pg27.jpg

## Slide 21: f10_02_pg28
COVALENT BONDING
Covalent
  sharing electrons
  Strong (Diamond) or weak (Bi)
  directional
H2, Cl2, F2
CH4, H20, HNO3, HF
Diamond, Si, Ge
GaAs, SiC
Notes: f10_02_pg28.jpg

## Slide 22: Primary Bonding
Ionic-Covalent Mixed Bonding
% ionic character =
where XA & XB are Pauling electronegativities
%)
100
(
x
Ex: MgO XMg = 1.3 XO = 3.5

## Slide 23: f11_02_pg30
METALLIC BONDING
Metallic
  metal ions in sea of electrons
  moderately strong
  68 kJ/mole – 850 kJ/mole
  non-directional
Good conductors of heat and electricity,
Ductile behavior
Notes: f11_02_pg30.jpg

## Slide 24: Secondary, Van der Waals, Physical bonds
  Arise from electrostatic attraction of electric dipole (local charge distribution)
  Weak 10 kJ/mole
  Effects obscured if primary bonds are present
  Occur between
    Induced dipoles
    Induced dipoles and polar molecules
    Polar molecules (Hydrogen Bonding)

## Slide 25: f13_02_pg31
Fluctuating Induced Dipole bonds
Instantaneous Short lived distortion of electrical symmetry
Vibrational motion of atoms
H2, Cl2
Attractive forces are temporary and fluctuate with time
Notes: f13_02_pg31.jpg

## Slide 26: f14_02_pg32
Polar Molecule - Induced Dipole bonds
In polar molecules: Permanent dipole moment exists as a result of asymmetrical arrangements of +vely and –vely charged atoms
Polar molecules can induce dipoles in adjacent nonpolar molecules
Attractive forces between polar molecule and induced dipole --> bond will form
Energy greater than that between two fluctuating induced dipoles
Notes: f14_02_pg32.jpg

## Slide 27: f14_02_pg32
Permanent Dipole bonds
Low molecular weight , However MP and BP very high
Van der Waals forces between adjacent polar molecules
Bond energy is significantly greater than that of between induced dipoles
Example of polar molecule bonding: Hydrogen bonding (strongest secondary bonding)
Occurs when hydrogen is covalently bonded to F, O, N
Single H electro is shared by other atom  H end of the bond is essentially a +vely charged bare proton that is unscreened by any electrons
Bond energy can be as high as 51 kJ/mole
Notes: f14_02_pg32.jpg

## Slide 28: f16_02_pg33
Water: Volume expansion upon freezing!!
9 volume % expansion upon freezing
Each water molecule participates in 4 hydrogen bonds 
Has 4 nearest neighbours
Open structure
Lower density
Solid ice structure
Liquid water
Structure partially broken – Molecules more closely packed together
Average number of nearest neighbours = 4.5
Melting
Notes: f16_02_pg33.jpg

## Slide 29
Water freezing into ice, by computer simulation. M. Matsumoto, S. Saito, and I. Ohmine, Molecular dynamics simulation of the ice nucleation and growth process leading to water freezing, Nature 416, 409-413 (2002)

## Slide 30: Summary
Subatomic (electronic) structure,
Periodic table,
Bond energy,
Inter-atomic/molecular bonding = f (electronic str.),
  Primary
    Metallic
    Ionic
    Covalent
  Secondary
Effects of sub-atomic structure and bonding on properties

## Slide 31: Students’ Presentations list
Sl. No. of allotment | Topic | Names | Roll
1 | Composite materials for aircraft (Topic 4) | Kailash Hudda | 16ME10031
 |  | Marghoob Kaifi | 16ME10041
 |  | Subodh Jain | 16ME10062
2 | Materials Damage in Nuclear Power Plant (Topic 6) | Ritvik Pandey | 16me30032
 |  | Ashwin Nehete | 16mf10035
 |  | Koumudi Mantha | 16me3fp07
3 | Ti Alloy for aerospace application (Topic 1) | Neelanjan Akuli | 16ME30049
 |  | Anjali Rao | 16MF3IM04
 |  | R Amartya | 16MF10034
4 | Ti alloy for biomaterial application (Topic 2) | PRAJWAL | 16ME30050
 |  | Siddhartha kapuria | 16ME30052
 |  | Akshay Jain | 16MF3IM02
5 | Ni based superalloy for gas turbine application (Topic 3) | Sangam | 16MF10023
 |  | Amit Pandey | 16ME10072
 |  | Shashwat Dixit | 16MF10032
6 | Metal Foams – Their Properties and Applications (Topic 5) | Debmalya Roy | 16ME10018
 |  | Debapriya De | 16ME10017
 |  | Jyotirmay Sahoo | 16ME10030